## Slide 1: Lab Course Cognitive Systems: Depth & Bounding Box Prediction
Final Presentation
WS 17/18
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 2
FCRN-SSD
3rd STAGE
ResNet50-Deconv + VGG16-SSD
FCRN-DSSD
Motivation
1st STAGE
Goal
Background
DeepTLR
2nd STAGE
Caffe
FZI
Future Work
6th STAGE
Improvements
Evaluation
5th STAGE
Results
Challenges
Solutions
4th STAGE
ResNet50-Deconv-SSD-Deconv

## Slide 3: 1. Motivation
Goal: Improve vehicle detections with CNN in real-time
Issues: poor performance for largely overlapping vehicles
Possible solution: using depth information to distinguish between overlapping vehicles
Evaluation of synthetic GTA V training data
1
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 4: 1. Motivation
Used datasets
2
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
KITTI 15k, 640 x 352, uint8/16 depth map
54205 boxes
GTA V 16k, 1280 x 720, uint8 depth map
80364 boxes
22.03.2018

## Slide 5: 2. DeepTLR+Conv
Joint convolution depth prediction and object detection:
Training with KITTI & GTA V images
Learning from depth images for monocular object detection with convolutional neural networks, MA A. Lesi
3
fc
ReLu
Dropout
Sigmoid
Feature Extraction
Feature Classific.
Class & BB Regression
640x352x3
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
AlexNet
22.03.2018

## Slide 6: 2. DeepTLR+Conv
Current results: Depth map prediction
6
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 7: 2. DeepTLR+Conv
Current results: Model trained on GTA V
7
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Inference on GTA V instance
Inference on KITTI instance

## Slide 8: 2. DeepTLR+Conv
Current results: Model trained on KITTI + GTA V
8
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Inference on GTA V instance
Compared to the Model trained only on KITTI

## Slide 9: 2. DeepTLR+Conv
Evaluation:
9
22.03.2018
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
 | Trained on KITTI |  | Trained on GTA V | 
 | Evaluated on KITTI testset | Evaluated on GTA V testset |  | Evaluated on KITTI testset
REL | 11.93 | 913.57 | 9259.95 | 180.84
RMSE | 13.78 | 75.86 | 15.60 | 156.47
LOG10 | 2.02 | 2.03 | 0.48 | 4.27
d1 | 0.04 | 0.01 | 0.65 | 0.002
d2 | 0.09 | 0.02 | 0.80 | 0.004
d3 | 0.17 | 0.03 | 0.88 | 0.007

## Slide 10: 3. FCRN-SSD
ResNet50 (fully convolution mode) and deconvolution layers:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
11
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Notes: Ansatz für die Depth Prediction basiert auf einem Paper
State of the Art im Vergleich zu anderen Netzarchitekturen
Eingabe des Netzes ist ein 304x228-Bild, Ausgabe ein Bild, das ungefähr halb so groß ist
Der Ansatz selbst basiert auf ResNet50 und erweitert diese Netzarchitektur,
Und zwar um ganz spezielle Deconvolution-Blöcke, sog. „Up-Convolutions“, die insb. die Geschwindigkeit des Netzes erhöhen

## Slide 11: 3. FCRN-SSD
Current results: Model trained on KITTI, inferenced on KITTI testset
14
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Notes: Jetzt einige Ergebnisse
Wir haben das FCRN auf KITTI trainiert und auf den KITTI-Testdatensatz angewandt
Links: KITTI-Bild, mitte: Lidar-Tiefendaten, und rechts die Vorhersage.
Was man sieht, ist, dass die Objekte aus dem Originalbild durchaus als Silhouetten in der Vorhersage erscheinen
  Sowohl der Fahrradfahrer, das Auto, und im oberen Bild die Ampel, und das Plakat
Auch sieht man einen Tiefenverlauf entlang des Straßenverlaufs

## Slide 12: 3. FCRN-SSD
Current results: Model trained on GTA V, inferenced on GTA V testset
16
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Notes: Dann hatten wir noch ein Modell auf GTA trainiert, und hier mal auf den GTA-Testdatensatz angewandt
In der Mitte sind die perfekten Tiefenbilder, die aus dem Spiel generiert wurden
Die meisten Objekte wurden hier erkannt, selbst die weiter entfernten Autos, oder die relativ dünne Ampel
Oder die Palme im unteren Bild

## Slide 13: 3. FCRN-SSD
Current results: Model trained on GTA V, inferenced on KITTI testset
18
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Notes: Interessanter ist jetzt die Inferenz vom GTA-trainierten Modell auf KITTI-Daten
Was hier vor allem auffällig ist, ist dass die näheren Objekte durchaus erkannt werden, die entfernteren Objekte aber nicht

## Slide 14: 3. FCRN-SSD
Evaluation:
18
22.03.2018
 | Trained on KITTI |  | Trained on GTA V | 
 | Evaluated on KITTI testset | Evaluated on GTA V testset |  | Evaluated on KITTI testset
REL | 11.93 | 913.57 | 9259.95 | 180.84
RMSE | 13.78 | 75.86 | 15.60 | 156.47
LOG10 | 2.02 | 2.03 | 0.48 | 4.27
d1 | 0.04 | 0.01 | 0.65 | 0.002
d2 | 0.09 | 0.02 | 0.80 | 0.004
d3 | 0.17 | 0.03 | 0.88 | 0.007
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski

## Slide 15: 3. FCRN-SSD
We chose the FCRN approach because of superior depth prediction performance
Deconvolutional network originally used for semantic segmentation did not train (with RMSE or Huber loss) and remained noisy
Next step: combining with bounding box prediction
Advantages of two isolated neural nets:
  Stable depth prediction
  Stable bounding box detection
  In multitask learning often hard to get loss function right
  Easier/better evaluation of GTA V data with two distinct networks
19
22.03.2018
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski

## Slide 16: 3. FCRN-SSD
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
20
22.03.2018
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
VGG16 (without fully connected layers) with auxillary SSD layers:
Notes: Basiert auf VGG16 und erweitert diesen um weitere Layer, welche die Feature Maps schrumpfen, auf den einzelnen Feature Maps wird mit Hilfe von Convlutions eine Klassifizierung ausgeführt.
Grundsätzlich ist die Idee: Es gibt zwei Teile im Netzwerk: Einer erzeugt Region Proposals verschiedener Größe, ein anderer klassifiziert.
Erzeugt sehr viele überlappende Detections, daher folgt ein Non-Maximum-Suppresion

## Slide 17: 3. FCRN-SSD
Multibox approach:
  Boxes will be estimated on multiple feature layers with different feature map sizes and default boxes
  Hard negative mining with ratio of negative to positive examples of around 3:1
21
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Notes: Auf die einzelnen Zellen der Feature Maps legt man gewisse Default-Boxen,
Die dann jeweils mit der Ground-Truth verglichen, man berechnet den IoU
und kann mit Hilfe dieser Kennzahl nun einen Pool aus negativen und positven Beispiel aufbauen
Zum Training nimmt man nun alle positiven Beispiele und die negativen Beispiele mit dem höchsten Loss, sodass kein Class Imbalance entsteht.

## Slide 18: 3. FCRN-SSD
22
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
RGBD
SSD
Aus FCRN

## Slide 19: 3. FCRN-SSD
Evaluation: Model trained on KITTI, inferenced on KITTI testset
22
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
 | Trained on KITTI
 | Evaluated on KITTI testset
mAP | 0.25
Notes: Bisher: Ein Training auf RGBD der GTA-Daten
Trainings-Loss konvergiert mit Tiefendaten schneller. Was wir allerdings noch nicht beantworten können, ist ob die Ergebnisse auch besser sind.
Im obigen Bild sieht man ein Beispiel, indem das auf GTA-trainierte Modell auf KITTI angewandt wurde,
Hier werden alle Autos erkannt, auch wenn relativ weit entfernt sind, mit relativ engen Bounding-Boxen
Allerdings gibt es sehr viele False Positives, was man hier an der Leitplanke ganz gut sieht.

## Slide 20: 4. FCRN-DSSD
End-to-end depth and bounding box prediction:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
23
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Deconvolution
48 x 48 x 512
FCRN
ResNet50
Deconvolution / Up-Projection
SSD
384 x 384 x 3
384 x 384 x 1
48 x 48 x 512
24 x 24 x 1024
12 x 12 x 1024
6 x 6 x 512
3 x 3 x 256
1 x 1 x 128
12 x 12 x 2048
PM
PM
PM
PM
PM
PM
DM
22.03.2018

## Slide 21: 4. FCRN-DSSD
Image Preprocessing:
Online image augmentation in Tensorflow
  Bounding box adjustments
  Random horizontal flip
  Random color distortion
  Patch sampling
24
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
1280 x 720 x 3
384 x 384 x 3

## Slide 22: 4. FCRN-DSSD
Current results:
25
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
GTA V
KITTI
Model trained on KITTI, inferenced on KITTI testset
Model trained on GTA V, inferenced on GTA V testset

## Slide 23: 4. FCRN-DSSD
Current results:
25
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
KITTI
KITTI
Model trained on KITTI, inferenced on KITTI testset
Model trained on GTA V, inferenced on KITTI testset

## Slide 24: 4. FCRN-DSSD
training is slow ~ 6 days, inference ~1s per batch  62,5 ms – 16 Hz
Evaluation:
18
22.03.2018
 | Trained on KITTI |  | Trained on GTA V | 
 | Evaluated on KITTI testset | Evaluated on GTA V testset |  | Evaluated on KITTI testset
REL | 199.94 | 188.51 | 65.82 | 62.57
RMSE | 205.92 | 195.99 | 92.71 | 81.22
LOG10 | - | - | 5.32 | -
d1 | - | - | - | -
d2 | - | - | - | -
d3 | - | - | - | -
mAP | 0.37 | 0.07 | 0.13 | 0.17
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski

## Slide 25: 5. Evaluation
RGB ranges:
28
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Red: KITTI, Blue: GTA V
Green: KITTI, Red: GTA V
Blue: KITTI, Green: GTA V
Red
Green
Blue

## Slide 26: 5. Evaluation
HSI ranges:
29
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Green: KITTI, Blue: GTA V
Green: KITTI, Red: GTA V
Blue: KITTI, Red: GTA V
Hue
Saturation
Intensity

## Slide 27: 5. Evaluation
30
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
KITTI
GTA V
22.03.2018
Bounding box distributions:

## Slide 28: 5. Evaluation
Bounding box positions:
31
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
KITTI
GTA V
22.03.2018

## Slide 29: 5. Evaluation
Summary:
Depth prediction trained on GTA V data works good, due to “perfect” data with all 3 approaches
Bounding box prediction with GTA V data is difficult and needs careful parameter choosing/tuning for all approaches
Using loss weights with 4:1 or 8:1 (DSSD:FCRN) when multitask training on GTA V or 1:4 when training on KITTI
GTA V trained networks works WELL/BAD on KITTI datasets …
32
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 30: 6. Future Work
Datasets:
Do offline preprocessing to handle ground truth bounding boxes out of range
Need to use more GTA V images ~ 200.000 images, since difference in images is very low
Adjust color ranges of GTA V data according KITTI and better in-game traffic flow control
Eliminate wrong bounding boxes due to insufficient occlusion handling in game – using stencil map for bounding box creation and matching with data needed
FCRN:
Using berHu loss instead of l2 norm (better results in paper), we already implemented it, but didn‘t train with
Combine KITTI and GTA datasets for training
SSD:
loss has problems to converge, especially for positive bounding box examples and localization; lots of small bounding boxes in GTA V data, better default box sizes, ratios and tiling needed
33
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 31: 6. Future Work
FCRN-DSSD:
Networks are in modular architecture, it’s easy to change certain parts/networks – trying other detectors
Extend code to support multiple GPUs for faster training, since a lot of trial and error is needed to get optimal loss weights, default box sizes, ratios, tiling etc.
If learning rate too high, SSD loss will oscillate, depth loss will converge fast
If learning rate too low, depth loss will not converge, SSD loss will oscillate less
Finding optimal weight for both loss function - Adaptive Loss Balancing
34
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 32
Questions?

## Slide 33
Backup

## Slide 34: 2. DeepTLR+Conv
Accomplished tasks:
  Caffe running
  Data processing & augmentation
  LMDB creation
  Training on KITTI
  Training on GTA V
  Training on mixed KITTI and GTA V
  Evaluation routines
  Using code from M. Weber and A. Lesi
  No modifications on framework planned
  Inference Speed: 20 – 45 ms
4
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 35: 2. DeepTLR+Conv
Loss during training:
5
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018

## Slide 36: 3. FCRN-SSD
Pretrained weights trained on NYU v2 dataset:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
10
22.03.2018
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski

## Slide 37: 3. FCRN-SSD
What was available with FCRN?
  Architecture in TensorFlow
  Evaluation Routines in Matlab
What have we done with FCRN?
  Architecture customized
  Data Processing
  Trainings Routines
  Training on KITTI data
  Training on GTA V data
  Evaluation Routines
12
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
300 px
300 px
22.03.2018
Notes: * Die Architektur dieses Netzes war verfügbar in TensorFlow, leider nicht die Trainingsroutine,
Und die Evaluationsroutine war in Matlab verfügbar, und damit eingeschränkt nutzbar.
Wir haben die Architektur leicht angepasst, sodass diese gleichgroße Bilder ausgibt, in unserem Fall ist Eingabe und Ausgabe 300x300
Dann haben wir einen TensorFlow-Data-Loader geschrieben, der die KITTI- und GTA-Daten lädt
Die Trainingsroutinen, sowie die Evaluationsroutinen,
Letztlich zwei Trainings ausgeführt: Auf KITTI und GTA

## Slide 38: 3. FCRN-SSD
13
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
L2 training loss:

## Slide 39: 3. FCRN-SSD
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
35
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
Up-Projection Module:

## Slide 40: 3. FCRN-SSD
Evaluation:
22
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
22.03.2018
*Training cancelled due to deadline of students in pool room
Depth Images are generated by FCRN (epoch no. 67 at time of writing)
Trained and Tested together with KITTI Object Challenge training dataset (60/40 split)
Optimizer: RMSProp
8 images / batch, lr: 0.001, weight_decay: 0.0005
Loss Function:

## Slide 41: 4. FCRN-DSSD
SSD Deconvolution Module:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
36
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Deconv layer H x W x 512
Feature layer (SSD)
2H x 2W x D
Deconv 2x2x512
Conv 3x3x512
BN
Conv 3x3x512
BN
ReLU
Conv 3x3x512
BN
Eltw. Product
ReLU
2H x 2W x 512
22.03.2018

## Slide 42: 4. FCRN-DSSD
SSD Prediction Module:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
37
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Feature Layer
Conv 1x1x256
Eltw. Sum
Loc Regress
Conv 1x1x256
Conv 1x1x1024
Cls
Conv 1x1x1024
22.03.2018

## Slide 43: 4. FCRN-DSSD
Loss functions:
Depth: berHu
SSD:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
38
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
,
22.03.2018

## Slide 44: 4. FCRN-DSSD
SSD Prediction Module:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
37
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Feature Layer
Conv 1x1x256
Eltw. Sum
Loc Regress
Conv 1x1x256
Conv 1x1x1024
Cls
Conv 1x1x1024
22.03.2018

## Slide 45: 4. FCRN-DSSD
SSD Prediction Module:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
37
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Feature Layer
Conv 1x1x256
Eltw. Sum
Loc Regress
Conv 1x1x256
Conv 1x1x1024
Cls
Conv 1x1x1024
22.03.2018

## Slide 46: 4. FCRN-DSSD
SSD Prediction Module:
Deeper Depth Prediction with Fully Convolutional Residual Networks, Laina et al.
+ SSD: Single Shot MultiBox Detector, Liu et al.
+ DSSD : Deconvolutional Single Shot Detector Fu et al.
37
S. Aklanoglu, J. Schuck, Y. El himer, F. Retkowski
Feature Layer
Conv 1x1x256
Eltw. Sum
Loc Regress
Conv 1x1x256
Conv 1x1x1024
Cls
Conv 1x1x1024
22.03.2018